## Slide 1: Digital Controls Final
Fall 2019
Noelle Lewandowski, Casey Bruno, Joao Barbosa,
Adam Pienkowski, and Don Webster

## Slide 2: System Architecture
keyboard_input.py
runcar.py
usb_cam
collectData.py
Notes: Noelle

## Slide 3: System Architecture (continued)
keyboard_input.py
  This sets up the keyboard input from a machine connected to the same ros network (publishes data to rostopic ‘driving’)
runcar.py
  This subscribes to the topic ‘driving’ and gets steering and speed data from keyboard, creates, and sends PWM signal
usb_cam
  ros package that streams usb_cam images
collectData.py
  Creates csv file by listening to the ‘driving’ topic and taking data from the usb_cam package
  Array where first two items are speed, and steering. The rest is the image’s data
  Each new row in the .csv is a new frame or change in speed/direction

## Slide 4: API Interface
usb_cam (in catkin_ws):
roslaunch usb_cam usb_cam-test.launch
runcar.py:
rosrun templecar runcar.py
collectData.py:
rosrun templecar collectData.py <filename.csv>
keyboard_input.py:
rosrun templecar keyboard_input.py
Notes: Problems:
Difficult to change image size leading to slow data recording
Unix cannot take keyboard input in python easily

## Slide 5: API Interfaces (continued)
Difficult to change image size leading to slow data recording
Unix cannot take keyboard input in python easily

## Slide 6: Data Collected (data)

## Slide 7: Data Collected (Image)

## Slide 8: Conclusion
Usage of ROS
  Allowed us to delegate different tasks to integrate later
  Can split computations to different machines
Control
  ‘WASD’-style controls to move car
Image processing
  Steering, speed, and image data saved to a CSV file
  Can be used as training data at a later date
Git: https://github.com/DonStoddard5/templecarmk3/blob/master/README.md
Notes: Don/Adam

## Slide 9: Future Work
Incremental steering and speed control
  Rewriting the keyboard commands to be more complicated
Save csv on separate machine
  Ros communication (Master URI)
Camera Image Data Compression
  compressed_image_transport ros package
Faster Data Recording
  Comes after compressed image data
Ros launch file
  runcar.py
  collectData.py; keyboard_input.py

## Slide 10: Future Work (continued)
Machine Learning for autonomous driving
  Training data required
Car doesn’t drive straight
  Weight distribution on car
Network Dropped
  Create a ‘safety’ where if no communication comes in for a certain amount of time, then it automatically shuts down